## Slide 1: Database Workloads on Ceph -- Are We There Yet?
Open Infra Summit, Denver
April 30, 2019
Paul Dardeau
Tushar Gohad

## Slide 2: Ceph
References: http://ceph.com/ceph-storage, http://thenewstack.io/software-defined-storage-ceph-way, https://www.openstack.org/analytics
Open-source, object-based scale-out storage
Object, Block and File in single unified storage cluster
Highly durable, available – replication, erasure coding
Runs on economical commodity hardware
13+ years of hardening, vibrant community
Scalability – CRUSH data placement, no single POF
Replicates and re-balances dynamically
Enterprise features – snapshots, cloning, mirroring
Most popular block storage for Openstack installs
Commercial support options from top ISVs

## Slide 3: Ceph Workloads and All-Flash Focus
* NVM – Non-volatile Memory
Notes: NVM -> Flash

## Slide 4: Ceph and PostgreSQL Integration Options
Deployment Considerations:
Bootable Ceph RBD Volumes (OS and PostgreSQL install)
PostgreSQL RBD Volumes (all-in-one or separate)
PostgreSQL
PostgreSQL
PostgreSQL
Bare Metal

## Slide 5: Different Block Storage Configs
Highest Performance - all NVMe, Xeon Platinum CPUs
  Lowest-latency
  Highest write throughput
  Most expensive
  Lower maximum capacity per node
Cost-Optimized - all flash, NVMe journals, Xeon Gold CPUs
  Good general purpose characteristics
  Balanced cost, performance, capacity
  Higher latency, lower cost, higher capacity
Today, we’re looking at Cost-Optimized configuration

## Slide 6: Test Environment Hardware - Ceph Cluster
Switches
Dell S3048-ON (cluster admin, iDRAC)
2x Dell S5248F-ON (48 port GbE, Ceph)
4x Ceph Storage Nodes
Dell PowerEdge R740xd, 2-socket Xeon Gold 6152 (22C)
192GB RAM, HBA330 JBOD controller, BOSS
2x Intel XXV710 25GbE NICs
2.5” drive chassis, 24 front drive bays
16x Intel S4600 SATA SSD, 960GB, data drives (OSD)
4x Intel P4600 NVMe 1.6TB, journaling (WAL/RocksDB)
Admin Node
Dell PowerEdge R640, 2-socket Intel Gold 6126
Notes: No separate nodes for MONs (all Ceph daemon containerized/colocated)
Starting configuration; suitable for POCs; starting point for production (ideally 5 nodes); scale to multi-rack deployments

## Slide 7: Test Environment Software and Configuration
4x Ceph Storage Nodes
RHEL 7.6, RHCS 3.2 (Luminous), BlueStore OSDs
Containerized (docker) Ceph daemons, MONs colocated with OSDs
16 OSDs per node (64 total), 4:1 ratio for data drives to NVMe
60TB raw storage, 20TB usable, 3x replication
2x dual-bonded 25GbE VLAN networks, fully fault tolerant, jumbo frames
1 Ceph pool (rbd), PGs=8192
10x Load Generation Nodes (PowerEdge R640)
RHEL 7.6
PostgreSQL 11.2, 5x DB server instances per node (50 total), untuned
250GB RBD data volume per DB server instance
40% (8TB) of cluster provisioned (24TB raw)

## Slide 8: Considerable Tuning of Ceph Cluster
Ceph tuning
  Finding 8192 as optimum PGs
  Use recently published best practices
OS tuning
  PID and file max
  VM
  Network stack read/write memory sizes
NUMA node PCIe slot assignments
  Separate 25GbE NICs
  Half of NVMe devices on each NUMA node
  Separate BOSS and JBOD controller
Hardware replacements
  Use P4600 NVMe instead of P4500
  Reduce number of SSD drives (20 to 16; 5:1 to 4:1)
  Use HBA330 instead of H740P controller
Final effect on 4KB random read:
Pre-tuning = 689,733 IOPS
Post-tuning = 1,493,349 IOPS
Gain = 116%

## Slide 9: NUMA Considerations - PCIe Slot Assignments

## Slide 10: FIO Benchmarks - librbd - 4KB Random Read

## Slide 11: FIO Benchmarks - librbd - 4KB Random Write

## Slide 12: Test Methodology - Sysbench
Configuration
  PostgreSQL configured to run bare-metal
  PostgreSQL configured with 25GB shared buffers
  250GB krbd volumes for data
  Sysbench configured to run bare-metal
Prepare x50
  Populate 14,000,000 records in 32 tables
Each Run x50
  5 minutes ramp (warmup) time
  5 minutes run time (data collection)
  Clear Ceph node caches between each test run:
  Drop Linux system caches
  Restart all OSDs
  Programmatically start all sysbench processes concurrently
  Run 1 sysbench process for each database server instance (50)
  Run sysbench on same node as DB it’s paired with

## Slide 13: Performance Results - 100% Read

## Slide 14: Performance Results - 100% Write

## Slide 15: Performance Results - Mixed 70/30 (R/W)

## Slide 16: Observations, Recommendations
Ceph is only getting better
  FileStore to BlueStore
  Ceph-deploy to ceph-ansible
  Calamari, rhscons, to Ceph Dashboard (Grafana/Prometheus)
  Can now deploy containerized and colocated daemons
Start slow, be deliberate (crawl, walk, run)
Understand drive failure, recovery and its impact on performance
Not fully turn-key (expect to build out some areas)
Don’t underestimate the importance of sizing and performance tuning
All-flash cost-optimized configuration is very good general purpose starting point.

## Slide 17: Looking forward ...

## Slide 18: High Performance All-NVMe Ready Architecture
4 Node, containerized/colocated Ceph daemons
Dual socket Xeon Platinum 8176 (Skylake, 28C)
2x Intel XXV710 25GbE NICs
Up to 12 Intel P4600 NVMe drives
2 or 4 OSDs per NVMe drive
Being optimized now, published RA in June 2019
Targeted for high performance, lowest-latency requirements

## Slide 19: Next Generation Intel® CPUs
Security Mitigations1
Leadership Performance
Higher Core Count, Frequencies
Intel® Optane™ DC Persistent Memory
Intel Deep Learning Boost (VNNI)
Optimized Frameworks & Libraries
1. No product or component can be absolutely secure

## Slide 20: Gaps in Memory-Storage Hierarchy

## Slide 21: Gaps in Memory-Storage Hierarchy

## Slide 22: Intel® Optane™ DC SSDs Operate Differently than NAND
Notes: Here’s another way to illustrate the difference between Intel Optane SSDs and NAND-based SSDs. NAND-based SSDs read and write in pages but erase only in blocks, usually in the background.
This creates a garbage collection process which negatively impacts performance.
However, Optane is bit addressable – you have the ability to write in place, without needing the ‘old’ data previously erased. So there's no garbage collection, which is one of the reasons Optane offers improved performance, especially for example read latency under write load.

## Slide 23: Intel® Optane™ - Lower and More Consistent Latency
1 Source – Intel-tested: Average read latency measured at queue depth 1 during 4k random write workload. Measured using FIO 3.1. Common Configuration - Intel 2U Server System, OS CentOS 7.5, kernel 4.17.6-1.el7.x86_64, CPU 2 x Intel® Xeon® 6154 Gold @ 3.0GHz (18 cores), RAM 256GB DDR4 @ 2666MHz. Configuration – Intel® Optane™ SSD DC P4800X 375GB and Intel® SSD DC P4600 1.6TB. Latency – Average read latency measured at QD1 during 4K Random Write operations using FIO 3.1. Intel Microcode: 0x2000043; System BIOS: 00.01.0013; ME Firmware: 04.00.04.294; BMC Firmware: 1.43.91f76955; FRUSDR: 1.43. SSDs tested were commercially available at time of test. The benchmark results may need to be revised as additional testing is conducted. Performance results are based on testing as of July 24, 2018 and may not reflect all publicly available security updates. See configuration disclosure for details. No product can be absolutely secure. Software and workloads used in performance tests may have been optimized for performance only on Intel microprocessors. Performance tests, such as SYSmark and MobileMark, are measured using specific computer systems, components, software, operations and functions. Any change to any of those factors may cause the results to vary. You should consult other information and performance tests to assist you in fully evaluating your contemplated purchases, including the performance of that product when combined with other products. For more complete information visit www.intel.com/benchmarks.
Write Pressure
(MB/s)
Average Read
Response Time (µs)
Time (Seconds)
Intel® Optane™ DC SSD
63x
lower
8x
lower
Random Write Pressure MB/s
Intel® SSD DC P4600
Intel® Optane™ SSD DC P4800X
Average Read Latency Under Random Write Workload
Notes: As you can see on the left hand side this chart, we’re measuring write pressure, on the right hand side we have average read response time.
The orange staircase is write pressure that we're applying to the drive. So we're increasing that write pressure over time and you can see initially, Optane is 8x faster than NAND SSDs.
But as the write pressure increases, the NAND SSD gets dramatically slower in its reads, whereas Optane more or less stays consistent in reads, leading to up to 63x lower average read response time.
This is powerful proof that Intel Optane SSDs are an excellent metadata drive for CEPH cluster.

## Slide 24: Intel® Optane™ SSDs
DC P4800X
DC P4801X
Results have been estimated or simulated using internal Intel analysis or architecture simulation or modeling, and provided to you for informational purposes. Any differences in your system hardware, software or configuration may affect your actual performance. 1See Product Specification for availability details
*Other names and brands may be claimed as the property of others.

## Slide 25: Ceph Bluestore Metadata – Collocated on data disk vs On Optane 4KB Random 50/50, QD=8
Better Latency
Consistency
With Optane for Ceph Metadata

## Slide 26: Next-Gen Cost-Optimized Solution
 |  | 5x Ceph Storage Nodes (Skylake + P4500 + P4600) | 5x Ceph Storage Nodes (Cascade Lake + P4320 + Optane)
CPU | SKU | Intel Xeon® Gold 6152 | Intel Xeon® Gold 6252
 | # of Cores | 2x 22 | 2x 24
 | Core Frequency | 2.1 GHz | 2.1 GHz
 | Cache Size | 1 MB L2, 30.25 MB L3 | 1MB L2, 35.75 MB L3
Memory | Total System Memory | 384 GB | 384 GB
Network | Bandwidth | 25x2 GbE | 25x2 GbE
Storage | OS Disk | Intel SSD DC S3610 1.5 TB | Intel SSD DC S3610 1.5 TB
 | Data | 6x Intel SSD DC P4500 4 TB (Data) | 6x Intel SSD DC P4320 8 TB (Data)
 | Metadata | Intel SSD DC P4600 2 TB (WAL/DB) | Intel SSD DC P4800X 375 GB (WAL/DB)
Cluster Configuration | Ceph Release | 13.2.4 Mimic | 13.2.4 Mimic
 | Number of OSDs/Disk | 2 | 2
 | Replication | 2x | 2x
 | Effective Capacity | 40TB | 80TB
Cascade Lake Processors = better core density at the same cost
3D-NAND P4320 QLC SSDs = better storage density at a lower price point
Optane P4800X SSDs for metadata = more IOPS, consistent latency

## Slide 27: Next-Gen Performance Solution
 |  | 5x Ceph Storage Nodes (Skylake + P4500 + P4600) | 5x Ceph Storage Nodes (Cascade Lake + P4510 + Optane)
CPU | SKU | Intel Xeon® Gold 6152 | Intel Xeon® Gold 6252
 | # of Cores | 2x 22 | 2x 24
 | Core Frequency | 2.1 GHz | 2.1 GHz
 | Cache Size | 1 MB L2, 30.25 MB L3 | 1MB L2, 35.75 MB L3
Memory | Total System Memory | 384 GB | 384 GB
Network | Bandwidth | 25x2 GbE | 25x2 GbE
Storage | OS Disk | Intel SSD DC S3610 1.5 TB | Intel SSD DC S3610 1.5 TB
 | Data | 6x Intel SSD DC P4500 4 TB (Data) | 6x Intel SSD DC P4510 4 TB (Data)
 | Metadata | Intel SSD DC P4600 2 TB (WAL/DB) | Intel SSD DC P4800X 375 GB (WAL/DB)
Cluster Configuration | Ceph Release | 13.2.4 Mimic | 13.2.4 Mimic
 | Number of OSDs/Disk | 2 | 2
 | Replication | 2x | 2x
 | Effective Capacity | 40TB | 40TB
Cascade Lake Processors = better core density at the same cost
3D-NAND P4510 TLC SSDs = 40% better write performance, higher endurance
Optane P4800X SSDs for metadata = more IOPS, consistent latency

## Slide 28: Gen-over-Gen Performance Improvements
Performance results are based on testing by Intel as of 2/20/2019 and may not reflect all publicly available security updates. See configuration disclosure for details. No product or component can be absolutely secure. Software and workloads used in performance tests may have been optimized for performance only on Intel microprocessors. Performance tests, such as SYSmark and MobileMark, are measured using specific computer systems, components, software, operations and functions. Any change to any of those factors may cause the results to vary. You should consult other information and performance tests to assist you in fully evaluating your contemplated purchases, including the performance of that product when combined with other products. For more complete information visit www.intel.com/benchmarks. Configurations: See next slide
Intel® SSD DC P4500
+
+
Intel® Xeon® Gold 6152 Processor + Intel® SSD DC P4600 + Intel® SSD DC P4500
Baseline
Up to 1.7X
Relative to Baseline
+
+
2nd Gen Intel® Xeon® Gold 6252 Processor + Intel® Optane™ SSD DC P4800X + Intel® SSD DC P4510
P4510
Up to 3.4X
Relative to Baseline
P4800X
Intel® SSD DC P4600
+
+
2nd Intel® Xeon® Gold 6252 Processor + Intel® Optane™ SSD DC P4800X + Intel® SSD D5-P4320
Intel® Optane™ SSD
P4320
Latest Gen Performance Solution
Latest Gen
Cost
Optimized Solution

## Slide 29: Gen-over-Gen Performance Improvements
Xeon Gold 6152 + Intel® SSD DC P4600 + Intel® SSD DC P4500
2nd Gen Intel® Xeon Gold 6252
+ Intel® Optane™ SSD DC P4800X + Intel® SSD DC P4510
IO Sizes
* Performance numbers are relative to Baseline
Performance results are based on testing by Intel as of 2/20/2019 and may not reflect all publicly available security updates. See configuration disclosure for details. No product or component can be absolutely secure. Software and workloads used in performance tests may have been optimized for performance only on Intel microprocessors. Performance tests, such as SYSmark and MobileMark, are measured using specific computer systems, components, software, operations and functions. Any change to any of those factors may cause the results to vary. You should consult other information and performance tests to assist you in fully evaluating your contemplated purchases, including the performance of that product when combined with other products. For more complete information visit www.intel.com/benchmarks. Configurations: See next slide
1.23X*
1.26X*
2.4X*
BASELINE
2nd Gen Intel® Xeon Gold 6252
+ Intel® Optane™ SSD DC P4800X + Intel® SSD D5-P4320
1.13X*
1.23X*
1.37X*
4KB
16KB
1MB
4KB
16KB
1MB

## Slide 30
Performance results are based on testing by Intel as of 2/20/2019 and may not reflect all publicly available security updates. See configuration disclosure for details. No product or component can be absolutely secure. Software and workloads used in performance tests may have been optimized for performance only on Intel microprocessors. Performance tests, such as SYSmark and MobileMark, are measured using specific computer systems, components, software, operations and functions. Any change to any of those factors may cause the results to vary. You should consult other information and performance tests to assist you in fully evaluating your contemplated purchases, including the performance of that product when combined with other products. For more complete information visit www.intel.com/benchmarks. Configurations: See next slide
4KB RANDOM
LATENCY Improvements
14%
READ
WRITE
26%
READ/WRITE
(70/30)
22%
19%
11%
10%
+
+
2nd Gen Intel® Xeon® Gold 6252 Processor + Intel® Optane™ SSD DC P4800X + Intel® SSD DC P4510
P4510
P4800X
P4500
+
+
Intel® Xeon® Gold 6152 Processor + Intel® SSD DC P4600 + Intel® SSD DC P4500
BASELINE
P4600
4KB RANDOM
LATENCY Improvements
Same
19%
11%
17%
25%
25%
+
+
2nd Gen Intel® Xeon® Gold 6252 Processor + Intel® Optane™ SSD DC P4800X + Intel® SSD D5-P4320
P4800X
P4320
Relative to BASELINE
Relative to BASELINE
Next-Gen Cost-Optimized
Next-Gen Performance

## Slide 31: Back to the question ...

## Slide 32: Are we there yet?
Yes, we’re there for vast majority of use cases
Some special cases could be challenging (outer edges)
Very good performance
Solid foundation and keeps getting better
Vibrant community

## Slide 33: Performance Improvements Pipeline
Client side caching
  Read-only and Crash-consistent Write-back Caching for block/object
  first sets of RO cache PRs merged upstream
Crimson OSD
  OSD re-architecture ( Seastar, DPDK, SPDK primitives – poll mode, lock-light )
  Red Hat and Intel leading
  Single threaded OSD, Seastar messenger prototypes in master
Block Client performance improvements
  Intel team leading RBD improvements for multithreading

## Slide 34: Questions, comments, sarcasm? :)

## Slide 36: NVM Express (NVMe) Standardized interface for non-volatile memory, http://nvmexpress.org
Source: Intel. Other names and brands are property of their respective owners. Technology claims are based on comparisons of latency, density and write cycling metrics amongst memory technologies recorded on published specifications of in-market memory products against internal Intel specifications.
Notes: NVM Express is an interface specification optimized for PCI Express® based storage solutions, such as solid-state drives. The NVMe 1.0 specification defines a scalable architecture that unlocks the potential of PCIe-based SSDs. With a throughput improvement of 6x and reduced storage latency over 6 Gbps SATA SSD, the Intel SSD PCIe Family increases processor utilization while scaling to meet demand.
NVM Express revolutionizes storage by delivering faster access to data and lowering latency and power consumption. NVM Express reduces latency, is achieved by eliminating the delay associated with memory adapters and optimizing the storage protocol that has limited SSD performance until now. NVMe reduces the number of layers in the storage protocol stack. Storage commands are processed with 60% fewer processor cycles and 60% less latency. These freed up processing cycle can now be used for real application workload, improving the efficiency of the processor.
NVMe delivers higher input/output operations per second (IOPS) and reduces power consumption for a lower total cost of ownership.
Segway: Intel sets itself apart from others by delivering the PCIe Family optimized for today’s mixed workload applications

## Slide 37: Databases, NVMe SSDs and Ceph
Why Databases?
  Databases among top-3 workloads on Openstack, Kubernetes
  (#1-2 host databases too)
Why NVMe SSDs?
  High IOPS
  Low, dependable latency
DBA-friendly Ceph feature-set
  Shared, elastic storage pools
  Snapshots (full and incremental) for easy backup
  Copy-on-write cloning
  Flexible volume resizing
  Live Migration
  Async Volume Mirroring